## Slide 1
on impact in plasma Electrophore model for dissociation of molecules after the electron impact in plasma
Ryan Brook,1,2 Dmitry Makhov,1 Alfred Stonelake,1 Gregory Armstrong,2 Anna Nelson,2 Jonathan Tennyson,2,3 and Dmitrii V. Shalashilin1* 1School of Chemistry, University of Leeds, Leeds LS2 9JT, United Kingdom 2Quantemol Ltd., 320 City Road, The Angel, London EC1V 2NZ, United Kingdom 3Department of Physics and Astronomy, University College London, London WC1E 6BT, United Kingdom *Email: d.shalashilin@leeds.ac.uk

## Slide 2: Motivation and vision.
Low temperature plasmas are essential to the manufacture of devices in the semiconductor industry.
Plasma Etching Plasma Deposition
Free radicals Ions Free Radicals
F•, •CF3, :CF2
+
Inside of a microchip

## Slide 3: Motivation and vision.
The gases are fluorine-organic molecules which are not environmentally friendly and expected to be phased out of manufacturing.
Developing new plasma sources with new families of gases, which are efficient and environmentally friendly, is a high priority for the industry.

## Slide 4
Experiment
Real plasma etching device coupled to quadruple Mass Spec. Etching patterns

## Slide 5
We run ab initio molecular dynamics (AIMC or AIMD) in order to identify:
  The fragments formed
  The kinetics of fragmentation
  Give us a molecule and we tell you how it breaks. In silico design?
Theory

## Slide 6
Molecular Dynamics we use
Alfred Stonelake
Sourav Roy
Ryan Brook
Dmitry Makhov
Plan of the talk
First simulations of dissociation of molecules after electron impact and Electrophore Model (EM)
https://doi.org/10.1021/acs.jpclett.4c00348
Development of Electrophore Model and systematic simulations of the dynamics with a new code.
https://doi.org/10.1116/6.0004454
https://etheses.whiterose.ac.uk/id/eprint/38227/
More simulations of dissociation of hydrofluorocarbons and electronic structure confirmation of the Electrophore Model
Future developments and vision. Potential energy surfaces with Machine Learning and simulations at low T. Better comparison with mass spec.

## Slide 7
mth electronic energy
Born-Oppenheimer electronic wave function of the mth electronic state (Adiabatic states)
PES drives the motion of nuclei
Basics. Born-Oppenheimer Potential Energy Surfaces and Molecular Dynamics.
But what are the surfaces involved in the dissociation in plasma?

## Slide 8
Basics. Born-Oppenheimer Potential Energy Surfaces and Molecular Dynamics.
Singlet state
Triplet state more repulsion
In plasma molecules are excited to higher electronic states by electron impact.
The lowest triplet electronic state plays crucial role in dissociation.

## Slide 9
S0
T1
A● + ●B
-
Basics. Born-Oppenheimer Potential Energy Surfaces and Mechanism of dissociation after electron impact
Several low electronic state both triplet and singlet can be excited by electron impact.
We expect that triplet states are most important as they are in general more repulsive and lower in energy
T2

## Slide 10
S0
S1
A● + ●B
Basics. Born-Oppenheimer Potential Energy Surfaces and Mechanism of photo-dissociation
In photochemistry only singlet states are excited by photons.
However, all method developed in photochemistry can be applied to chemistry after electron impact
S2
hν

## Slide 11
Ehrenfest configuration
is a Gaussian CS dressed with Electronic wave function
Amplitude
Sum of normalised Ehrenfest configurations
Non-adiabatic quantum dynamics
We apply our own Ab Initio Multiple Cloning (AIMC) method.
Nuclear basis of Gaussian CSs
Electronic wave function

## Slide 12: Non-adiabatic quantum dynamics
We apply our own Ab Initio Multiple Cloning (AIMC) method.
Coherent State Samplings:
Cloning
Cloning is a straightforward
way to do spawning (Martinez)
Cloning provides adoptive basis set for nonadiabatic dynamics

## Slide 13: Non-adiabatic quantum dynamics
We apply our own Ab Initio Multiple Cloning (AIMC) method.
AIMC describes quantum motion of nuclei in terms of several coupled trajectory guided basis functions.
Cloning provides trajectory branching to account for wave-function bifurcation when there are transitions between electronic states.
Forces are calculated Ab initio
If we use only one trajectory and one PES then AIMC becomes Ab Initio Molecular Dynamics AIMD.

## Slide 14
First simulations of dissociation of molecules after electron impact and Electrophore Model (EM)
https://doi.org/10.1021/acs.jpclett.4c00348
Dmitry Makhov
C3H2F6
C3H2F4

## Slide 15: Molecules
Two molecules has been chosen for the start, C2H2F4 and C3H2F6
C2H2F6
C2H2F4
One clearly separated lowest triplet state
Can avoid expensive non-adiabatic dynamics
No separation between two lowest excited states
Non-adiabatic dynamics is needed
Electron impact excitation cross sections for C3H2F6 and C3H2F4

## Slide 16: Non-adiabatic dynamics for C2H2F6
Average populations of the upper triplet state of C3H2F6 molecule as a function of time given by AIMC nonadiabatic dynamics calculations that use lower (blue) and upper (red) triplet states as the initial state.
Even when several triplet states are initially involved, in many cases higher triplet states quickly relax into the lowest triplet state.
Spin-flip TDDFT method implemented in Q-Chem quantum chemistry package (BH&HLYP, 6-31+G*)
500 trajectories with Boltzmann random initial conditions for 5000 K

## Slide 17: Dissociation kinetics of C2H2F6
Comparison of dissociation kinetics of a C3H2F6 given by AIMC nonadiabatic dynamics with initial state T2 (solid) and by the molecular dynamics (AIMD) on T1 potential energy surface (dashed). The number of broken bonds as a function of time for at 5000 K.
For all other molecules, we run molecular dynamics on a single T1 potential energy surface.
T2
T1
-

## Slide 18: Dissociation kinetics of C2H2F4
C-C bond breaks efficiently
C=C bond breaks very fast initially
C-F bond at double-bonded C atom has significantly higher dissociation rate than other C-F bonds
This can be explained by the localization of the initial T1 excitation on the double bond.
The double bond here can be called an electrophore, by analogy with the chromophore in photochemistry.
The number of broken bonds as a function of time
for C3H2F4 at 5000 K.
The electrophore model can help to predict the dissociation channels

## Slide 19: Electrophores
pz
sp2
σ*
π*
π
σ
pz
sp2
O sp3
C
C
(a)
(b)
Triplet excitation is localized in the region with a low energy gap between the highest occupied and the lowest unoccupied orbitals
(a) The energy gap between π- and π*-orbital is low, which makes C=C bond an electrophore
(b) The lone pairs of the oxygen atom do not participate in chemical bonding, and their energy is in the middle between those of the bonding andantibonding orbitals.
The energy gap is lower than for promoting an electron from the bonding to the antibonding orbital
This makes oxygen atom a possible electrophore.
Are there other types of Electrophore?

## Slide 20
Ryan Brook
Development of Electrophore Model and systematic simulations of the dynamics with a new code.
https://doi.org/10.1116/6.0004454
https://etheses.whiterose.ac.uk/id/eprint/38227/

## Slide 21
Ryan Brook
Development of Electrophore Model and systematic simulations of the dynamics with a new code.
https://doi.org/10.1116/6.0004454
https://etheses.whiterose.ac.uk/id/eprint/38227/
We have chosen a new selection of fluorinated organic molecules, now with an oxygen atom.
These molecules were investigated experimentally, and several key bonds were identified to be prominent in their neutral dissociation pathways.
PPVE
n-C4H3F7O
i-C4H3F7O
C4H2F7OH

## Slide 22: i-C4H3F7O – Overview
C-O bonds break most
One C-H bond breaks for every molecule
C-F has the lowest number of bonds broken
1
2
3
4

## Slide 23: n-C4H3F7O – Overview
C-C bonds break similar to the case of i-isomer, but other bonds break less frequently
1
2
3
4

## Slide 24: n- vs i-isomer – C-C
1
2
3
4
1
2
3
4
The C#2-C#3 bonds in the n-isomer breaks much more often
This can be explained by the proximity to the oxygen atom, which is an electrophore in this molecule
The C-C bonds in the i-isomer breaks with the same rate, as to be expected from a symmetrical molecule.

## Slide 25: n- vs i-isomer – C-F
1
2
3
4
1
2
3
4
The breaking rate of C-F bond in n-isomer greatly dependent on the proximity to the oxygen atom.
For i-isomer, the C#2-F bond breaking rate is the highest.
Oxygen atom is an electrophore

## Slide 26: PPVE – Overview
C=C & C-O bonds break the most, suggesting location of localization
1
2
3
4
5

## Slide 27: PPVE – C-F Bonds
Over 50% of all C-F bonds broken come from just one single C-F bond
The effect of proximity to multiple electrophores is cumulative
1
2
3
4
5
PPVE molecule has two electrophores – a double bond and an oxygen atom.

## Slide 28: PPVE – Low C#3-F Count
C#3-O quickly breaks in 66% of the molecules due to the presence of the double bond.
C#2-C#3 breaks in 40.5% of molecules
Both of these factors combined limit the breaking of the C#3-F bonds, despite proximity to the oxygen atom.
1
2
3
4
5

## Slide 29: C4H2F7OH – Overview
O-H bond breaks almost immediately
Probably this prevents C-O bond breaking
1
2
3
4

## Slide 30: Experimental
Y.Kim et al, ACS Sustainable Chemistry & Engineering, 2022, 10, 32, 10537–10546. https://doi.org/10.1021/acssuschemeng.2c01705
The molecules that we simulated were investigated experimentally to test whether they would be viable replacements for the C4F8 plasma precursor
Several key bonds were identified to be prominent in their neutral dissociation pathways.
These bonds correspond to the bonds most often dissociated in our simulations.

## Slide 31
Experimental
Real plasma etching device couple to quadruple Mass Spec. Etching patterns

## Slide 32
Dissociation rules
Based on the results for all molecules, we have formulated a preliminary list of rules for triplet state dissociation
Selected rules:
Double C=C bonds and an oxygen atoms are electrophores
Bonds in the proximity of the electrophore dissociate more efficiently
The effect of proximity to multiple electrophores is cumulative
Detailed list of rules is in our paper

## Slide 33
Alfred Stonelake
More simulations of dissociation of hydrofluorocarbons and electronic structure confirmation of the Electrophore Model

## Slide 36
Mass Spec (blue) at 300 K vs MD product distribution (red) at 5000 K
To make quantitative comparison we need :
To take into account dissociation of radicals after ionization
To take into account reactions in plasma
To reduce the temperature of the simulations to hundreds of K !!!

## Slide 37
Sourav Roy
Future developments and vision. Potential energy surfaces with Machine Learning and simulations at low T. Better comparison with mass spec.
1) Machine Learning Force Field instead of ab initio dynamics will speed up calculations. Currently we can go down to 2000-3000 K
2) Better ways to compare with mass spec
4) Vision: Tell us the radicals you want, and we suggest molecules to put into your plasma
3) More molecules, more types of electrophores.

## Slide 38: Summary
Dissociation of lowest excited triplet state following electron impact excitation is important for industry but has been very little investigated.
Electrophores, i.e., a small parts of the molecule that localize the initial triplet excitation, exist, such as C=C double bond or oxygen atom.
The bonds containing the electrophore dissociate readily, and the proximity to the electrophore also affects the dissociation yield of other chemical bonds.
For more details see the link from our group webpage: https://molecular-dynamics.leeds.ac.uk/neutral-dissociation-in-plasma/
Thank you!